## Slide 1: ENGI 301 Skittle Dispenser Proposal
10/3/2018
Nicholas Lester

## Slide 2: Background Information
I am proposing to make a Skittle dispenser with the following functions:
  Dispense candy with an IR sensor
  Display the current fill level as a percentage of “full” by measuring the weight of candy
  Give audio feedback when dispensing
  Stretch goal: Send notifications over a network when fill level is low

## Slide 3: Container Design Sketch
The weight to fullness equation will be calculated through trial as the container is not a simple rectangle (there is the slant).
There will be some inaccuracy of the fullness measurement when the container is very close to empty.

## Slide 4: Background Information
Existing project: https://www.hackster.io/hadamiera/candy-dispenser-a61a60
Improvements: By structuring the design differently and adding a weight sensor, you will be able to know how much candy you have left in the dispenser.
Existing project

## Slide 5: System Block Diagram
PocketBeagle
MicroUSB
USB0
PWM1
Micro Servo
AIN_IN
FSR
I2C1_SCL
I2C1_SDA
Adafruit 4-Digit Display
GPIO
IR Sensor
Piezo Element

## Slide 6: Power Block Diagram
PocketBeagle
MicroUSB
VIN_USB
SYS_VOUT
Micro Servo
3.3V_OUT
FSR
3.3V_VOUT
Adafruit 4-Digit Display
3.3 Volts
~ 160 mA
3.3 Volts
5 Volts
~ 1 mA
5 Volts
3.5 mA
Piezo Element
IR Sensor Part 2
IR Sensor Part 1
SYS_VOUT
5 Volts
20 mA total
SYS_VOUT
5 Volts
~ 3 mA

## Slide 7: Components / Budget
Component | Need to Buy | Cost
Micro Servo (Adafruit) | 1 | $5.95
Square Force-Sensitive Resistor (FSR) – Interlink 406 | 1 | $8.95
IR Break Beam Sensor - 3mm LEDs | 1 | $1.95
Large Enclosed Piezo Element w/Wires | 1 | $0.95
Resistors | 0 | 
PocketBeagle | 0 | 
Adafruit 0.56" 4-Digit 7-Segment Display w/I2C Backpack | 0 | 
Breadboard | 0 |